## Slide 1: Figure 3: Renewables shares 2017-2030 [%]. The renewables shares is calculated as defined in the RE Directive (Eurostat, 2018).
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
RE Share (RES) | 0.3425 | 0.37435 | 0.38901 | 0.41078 | 0.42524 | 0.44705 | 0.45569 | 0.46518 | 0.47122 | 0.49518 | 0.50407 | 0.51489 | 0.52518 | 0.54198
RE Share Electricity (RES-E) | 0.6375 | 0.7067 | 0.72605 | 0.76594 | 0.80415 | 0.84783 | 0.85561 | 0.87722 | 0.88473 | 0.9818 | 0.99192 | 1.0182 | 1.0385 | 1.0887
RE Share Transportation (RES-T) | 0.066695 | 0.069577 | 0.074665 | 0.08673 | 0.083326 | 0.088183 | 0.093447 | 0.101 | 0.10679 | 0.11403 | 0.13785 | 0.15396 | 0.16972 | 0.18606
RE Share Heating and Cooling (RES-H&C) | 0.44427 | 0.48139 | 0.50355 | 0.53514 | 0.54478 | 0.56555 | 0.57421 | 0.57826 | 0.58221 | 0.58292 | 0.58658 | 0.59067 | 0.59578 | 0.59897
RE Share District Heating (RES-DH) | 0.55051 | 0.63848 | 0.67184 | 0.70725 | 0.72392 | 0.74394 | 0.76282 | 0.76898 | 0.77571 | 0.7741 | 0.77782 | 0.78276 | 0.79034 | 0.79282

## Slide 2: Figure 4: Gross energy consumption by type of energy 1990-2030 [PJ]. The calculation for 1990-2017 has been adjusted for outdoor temperature/degree days relative to normal years (climate-adjusted) and electricity trade with other countries (electricity-trade adjusted, see Appendix 2).
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Coal | 326.9761 | 329.9734 | 323.7715 | 312.7834 | 300.6284 | 264.5989 | 242.246 | 220.5604 | 197.8693 | 180.798 | 175.3844 | 167.4034 | 161.5075 | 176.3422 | 163.0564 | 165.5199 | 182.0368 | 191.9994 | 186.4686 | 171.9636 | 147.3402 | 149.1881 | 146.8592 | 140.6136 | 129.6855 | 110.7158 | 116.417 | 91.6747 | 61.9715 | 65.3598 | 50.5552 | 40.1048 | 39.3048 | 27.4868 | 29.007 | 29.3445 | 29.1842 | 27.7606 | 26.654 | 12.8438 | 12.7548
Oil | 354.8487 | 354.8838 | 348.5489 | 345.0762 | 346.8351 | 374.129 | 380.8649 | 383.4352 | 379.2674 | 382.3893 | 376.3668 | 376.8407 | 361.2704 | 344.8977 | 348.8383 | 351.869 | 346.4894 | 346.7008 | 338.3858 | 314.3915 | 311.8845 | 303.9387 | 291.4469 | 280.8334 | 274.7595 | 279.1693 | 279.7997 | 285.802 | 285.7117 | 286.2655 | 285.6337 | 285.4398 | 285.2626 | 284.8276 | 283.9591 | 283.176 | 282.0049 | 278.8237 | 277.1241 | 274.8219 | 272.7424
Natural gas | 81.7759 | 87.1887 | 94.7185 | 102.1881 | 117.1881 | 133.7547 | 150.5965 | 166.696 | 181.0725 | 192.0718 | 192.1091 | 193.059 | 195.8992 | 190.1592 | 195.0416 | 192.4765 | 190.7445 | 175.2932 | 177.0787 | 166.2745 | 175.8875 | 159.7971 | 149.3206 | 139.6336 | 130.2105 | 132.952 | 131.1747 | 124.7081 | 108.519 | 99.817 | 91.1317 | 89.1794 | 84.3292 | 84.8148 | 83.1465 | 80.325 | 75.3488 | 74.9827 | 74.7872 | 74.2632 | 74.5204
MSW (fossil share) | 7.7096 | 7.6611 | 8.4713 | 8.6472 | 9.4427 | 10.4303 | 10.6394 | 12.2953 | 12.2178 | 13.6029 | 14.4018 | 14.5297 | 15.7425 | 16.7114 | 17.0784 | 17.3052 | 17.7466 | 18.4798 | 19.172 | 17.8208 | 16.3412 | 17.6211 | 16.7543 | 16.8183 | 18.3126 | 18.3075 | 17.9729 | 18.1133 | 18.7174 | 18.494 | 18.4819 | 18.4997 | 18.4874 | 18.495 | 18.5063 | 18.0018 | 17.9917 | 17.984 | 17.9791 | 17.9625 | 17.5754
Renewable energy | 47.7391 | 49.7649 | 53.8179 | 54.3916 | 55.3441 | 57.2251 | 58.5661 | 65.5925 | 68.6121 | 72.7338 | 80.6565 | 85.0209 | 92.4765 | 104.7889 | 115.5146 | 123.0881 | 126.4751 | 140.8819 | 141.7577 | 142.4379 | 162.9095 | 175.0066 | 179.9107 | 187.1623 | 202.1388 | 218.5094 | 224.7176 | 252.1084 | 275.3309 | 284.3449 | 298.0372 | 310.0335 | 326.6868 | 334.0697 | 342.2553 | 347.7571 | 365.3832 | 372.1998 | 380.3224 | 387.8993 | 400.1086

## Slide 3: Figure 5: Final energy consumption by consumption sector 1990-2030 [PJ].
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Non-energy | 13.0042 | 12.7401 | 12.8816 | 13.2622 | 13.2189 | 13.4031 | 14.2947 | 13.9289 | 12.5575 | 13.2014 | 12.6189 | 11.1633 | 11.2561 | 11.6302 | 12.9009 | 12.0644 | 12.2181 | 12.9645 | 11.034 | 10.4979 | 11.0263 | 12.3736 | 11.524 | 11.6359 | 10.5501 | 10.5292 | 10.4915 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497 | 10.3497
Households | 185.0392 | 186.8709 | 187.4728 | 190.1654 | 192.377 | 192.209 | 189.0182 | 194.4025 | 193.8719 | 192.9968 | 189.2746 | 187.613 | 191.0761 | 191.4128 | 191.9604 | 194.7288 | 199.0612 | 201.0493 | 198.2142 | 191.6171 | 191.5847 | 195.0946 | 184.8095 | 186.7246 | 189.3567 | 193.0356 | 195.478 | 193.9125 | 193.4382 | 192.705 | 191.9718 | 190.942 | 189.9122 | 188.8824 | 187.8526 | 186.8228 | 185.6802 | 184.5375 | 183.3949 | 182.2522 | 181.1096
Transport | 170.2164 | 175.7572 | 173.8555 | 175.5034 | 180.8171 | 184.3579 | 188.1529 | 191.0363 | 193.3717 | 199.0984 | 201.2092 | 201.1431 | 197.4562 | 201.9041 | 210.6795 | 215.789 | 217.7252 | 224.0196 | 221.5538 | 208.3507 | 209.7315 | 210.2259 | 207.2564 | 205.2593 | 207.2581 | 209.2651 | 213.8285 | 218.253 | 219.9633 | 221.6399 | 222.8392 | 223.7117 | 224.3749 | 224.9047 | 225.2098 | 225.332 | 225.2889 | 224.8364 | 224.4443 | 223.8647 | 223.1369
Manufacturing | 158.1881 | 163.9231 | 164.7474 | 160.747 | 164.0804 | 167.1825 | 167.5064 | 170.9051 | 167.689 | 169.6433 | 166.8038 | 167.4974 | 160.4916 | 159.635 | 159.6827 | 158.1497 | 162.3162 | 157.3006 | 152.3764 | 135.674 | 137.2329 | 138.5384 | 129.7806 | 124.9761 | 122.6836 | 125.0443 | 126.6588 | 129.5281 | 129.8993 | 130.2774 | 130.6556 | 131.5023 | 132.349 | 133.1958 | 134.0425 | 134.8893 | 135.0979 | 135.3065 | 135.5151 | 135.7236 | 135.9322
Service | 77.0468 | 75.7987 | 76.7473 | 76.5677 | 76.6971 | 77.6918 | 79.591 | 80.7154 | 80.404 | 80.8625 | 80.5993 | 79.7518 | 82.9671 | 84.0946 | 84.8965 | 85.0445 | 87.7021 | 86.7851 | 86.7791 | 84.2375 | 83.8934 | 83.2813 | 82.061 | 81.9116 | 81.6223 | 81.2724 | 82.138 | 84.7636 | 85.3184 | 86.6677 | 89.6 | 93.6319 | 97.5847 | 101.3001 | 104.6989 | 107.7812 | 110.5974 | 113.1762 | 115.6759 | 118.1755 | 120.6751

## Slide 4: Figure 6: Electricity consumption (excluding grid losses) by use 2017-2030 [PJ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Other industry and services, househ. appls. | 96.1192 | 96.8333 | 97.5515 | 98.2696 | 99.1975 | 100.1254 | 101.0533 | 101.9812 | 102.9091 | 103.352 | 103.7948 | 104.2377 | 104.6806 | 105.1234
Heat pumps, electric boilers, electric heating | 10.3118 | 12.1853 | 13.0781 | 12.2245 | 15.0048 | 17.7465 | 19.6891 | 21.1226 | 22.4857 | 23.0641 | 23.9881 | 25.1799 | 26.2544 | 26.879
Process heat (industry) | 6.4897 | 6.2282 | 5.9667 | 5.7051 | 5.5819 | 5.4586 | 5.3353 | 5.212 | 5.0887 | 4.974 | 4.8593 | 4.7446 | 4.6299 | 4.5151
Electric vehicles | 0 | 0.19073 | 0.27759 | 0.40797 | 0.56405 | 0.7301 | 0.89935 | 1.0828 | 1.3075 | 1.5963 | 1.9632 | 2.4181 | 2.9703 | 3.626
Rail transport (and maritime) | 1.4654 | 1.5182 | 1.5628 | 1.6074 | 1.6309 | 1.6355 | 1.6611 | 1.9971 | 2.0022 | 2.0073 | 3.5833 | 3.7138 | 3.8503 | 3.8875
Data centres | 0 | 0 | 0.79142 | 3.1657 | 6.3314 | 9.4179 | 12.2671 | 14.7996 | 17.0156 | 18.915 | 20.577 | 22.1598 | 23.7427 | 25.3255

## Slide 5: Figure 7: Electricity consumption (excluding grid losses) by use in 2030 [%].
Chart: 
| Data centres | Electric vehicles | Rail transport (and maritime) | Other industry and services, househ. appls. | Process heat (industry) | Heat pumps, electric boilers, electric heating
 | 25.3255 | 3.626 | 3.8875 | 105.1234 | 4.5151 | 26.879

## Slide 6: Figure 8: Macro-economic energy intensity measured in relation to gross energy consumption and final energy consumption 2017-2030 [TJ per DKK mill.].

## Slide 7: Figure 9: Final energy consumption by households for heating 2017-2030 [PJ]. Gas comprises mains gas, i.e. natural gas, gas works gas and bio-natural gas. Other renewable energy includes firewood in particular, but also solar heating and straw.
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Oil | 8.9613 | 8.4847 | 7.6919 | 6.8991 | 6.3715 | 5.8439 | 5.3163 | 4.7887 | 4.2611 | 3.9125 | 3.5638 | 3.2151 | 2.8664 | 2.5178
Gas | 26.5334 | 26.2294 | 26.0188 | 25.8081 | 25.543 | 25.2779 | 25.0128 | 24.7477 | 24.4826 | 23.9131 | 23.3437 | 22.7742 | 22.2047 | 21.6352
Wood pellets | 14.8965 | 14.7284 | 14.5604 | 14.3924 | 13.9217 | 13.451 | 12.9804 | 12.5097 | 12.0391 | 11.5094 | 10.9797 | 10.45 | 9.9204 | 9.3907
Electricity | 5.3599 | 5.6622 | 5.9645 | 6.2669 | 6.4187 | 6.5706 | 6.7224 | 6.8742 | 7.0261 | 7.2495 | 7.4729 | 7.6963 | 7.9197 | 8.1431
Ambient heat | 6.4855 | 7.5083 | 8.5311 | 9.5539 | 10.1949 | 10.8359 | 11.477 | 12.118 | 12.7591 | 13.6498 | 14.5405 | 15.4312 | 16.322 | 17.2127
District heating | 71.37 | 70.6922 | 70.0144 | 69.3366 | 69.0213 | 68.7059 | 68.3906 | 68.0752 | 67.7598 | 67.5142 | 67.2685 | 67.0228 | 66.7771 | 66.5314
Other renewables | 29.1953 | 28.8989 | 28.6025 | 28.3061 | 27.9713 | 27.6365 | 27.3017 | 26.9668 | 26.632 | 26.1343 | 25.6365 | 25.1388 | 24.641 | 24.1433

## Slide 8: Figure 10: Final energy consumption by households analysed by selected heating technologies 2017-2030 [PJ]. Energy consumption by heat pumps includes ambient heat and electricity consumption. Gas comprises natural gas, gas works gas and bio-natural gas. District heating and fuel wood have been excluded.
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Oil boilers | 8.9613 | 8.4847 | 7.6919 | 6.8991 | 6.3715 | 5.8439 | 5.3163 | 4.7887 | 4.2611 | 3.9125 | 3.5638 | 3.2151 | 2.8664 | 2.5178
Gas boilers | 26.5334 | 26.2294 | 26.0188 | 25.8081 | 25.543 | 25.2779 | 25.0128 | 24.7477 | 24.4826 | 23.9131 | 23.3437 | 22.7742 | 22.2047 | 21.6352
Wood pellet boilers | 14.8965 | 14.7284 | 14.5604 | 14.3924 | 13.9217 | 13.451 | 12.9804 | 12.5097 | 12.0391 | 11.5094 | 10.9797 | 10.45 | 9.9204 | 9.3907
Electric heating | 2.4093 | 2.3353 | 2.2637 | 2.1921 | 2.1165 | 2.041 | 1.9655 | 1.8899 | 1.8144 | 1.7436 | 1.6728 | 1.602 | 1.5312 | 1.4604
Heat pumps | 9.4361 | 10.8352 | 12.2319 | 13.6287 | 14.4971 | 15.3655 | 16.2339 | 17.1023 | 17.9707 | 19.1557 | 20.3406 | 21.5255 | 22.7105 | 23.8954

## Slide 9: Figure 11: Number of electrical appliances [Index] and developments in electricity consumption by use: electronic equipment, electrical appliances and lighting 2017-2030 [TWh].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Electronics | 3.814 | 3.8497 | 3.8854 | 3.9211 | 3.9431 | 3.9652 | 3.9872 | 4.0093 | 4.0313 | 4.0258 | 4.0204 | 4.0149 | 4.0094 | 4.0039
Household appliances | 3.5726 | 3.6164 | 3.6602 | 3.704 | 3.737 | 3.7701 | 3.8032 | 3.8362 | 3.8693 | 3.8702 | 3.8711 | 3.872 | 3.873 | 3.8739
Lighting | 1.0158 | 0.98575 | 0.95568 | 0.9256 | 0.91245 | 0.8993 | 0.88616 | 0.87301 | 0.85987 | 0.85727 | 0.85467 | 0.85206 | 0.84946 | 0.84686
Number of appliances (index 2017=100) | 100 | 102.9415 | 105.8831 | 108.8246 | 111.7662 | 114.7077 | 117.6492 | 120.5908 | 123.5323 | 125.727 | 127.9216 | 130.1163 | 132.311 | 134.5056

## Slide 10: Figure 12: Final energy consumption by industry and services by type of energy 2017-2030 [PJ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Fossil fuels | 83.319 | 82.891 | 81.638 | 79.5315 | 79.3484 | 76.8734 | 76.872 | 76.8751 | 76.9542 | 76.6152 | 76.4013 | 76.2064 | 76.0562 | 75.8425
Renewable energy | 17.19 | 18.1983 | 19.9027 | 22.5218 | 23.4574 | 26.5278 | 27.2215 | 27.932 | 28.5353 | 29.4696 | 30.3856 | 31.2872 | 32.1467 | 33.0473
District heating | 38.0373 | 38.1042 | 38.1714 | 38.2387 | 38.5245 | 38.8103 | 39.0962 | 39.382 | 39.6678 | 39.5999 | 39.532 | 39.4641 | 39.3962 | 39.3283
Electricity excl. data centres | 75.7453 | 76.1007 | 76.4602 | 76.8196 | 77.547 | 78.2744 | 79.0018 | 79.7292 | 80.4566 | 80.9406 | 81.4246 | 81.9086 | 82.3926 | 82.8767
Electricity for data centres | 0 | 0 | 0.79142 | 3.1657 | 6.3314 | 9.4179 | 12.2671 | 14.7996 | 17.0156 | 18.915 | 20.577 | 22.1598 | 23.7427 | 25.3255

## Slide 11: Figure 13: Final consumption of fossil fuels by industry and services by sector 2017-2030 [PJ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Agriculture and fishery | 19.8679 | 19.8872 | 19.8716 | 19.8138 | 19.9749 | 20.0345 | 20.2041 | 20.3726 | 20.5459 | 20.4181 | 20.2912 | 20.165 | 20.0409 | 19.9147
Construction | 5.7629 | 5.7945 | 5.8199 | 5.8371 | 5.8853 | 5.9145 | 5.9647 | 6.0146 | 6.0655 | 6.0677 | 6.0701 | 6.0727 | 6.0756 | 6.0782
Manufacturing | 46.9689 | 46.5019 | 45.5504 | 43.9324 | 43.6479 | 41.7975 | 41.6909 | 41.5721 | 41.532 | 41.3979 | 41.2775 | 41.1682 | 41.0899 | 40.9821
Service | 10.7193 | 10.6308 | 10.3775 | 9.9264 | 9.7657 | 9.1568 | 9.0496 | 8.9393 | 8.8517 | 8.8865 | 8.9245 | 8.9652 | 9.0145 | 9.0547

## Slide 12: Figure 14: Industry and services’ consumption of different types of energy by use in 2030 [PJ] and share of fossil fuels [%]. Coal includes coal, coke, petroleum coke and fossil waste. Gas comprises mains gas that includes both natural gas and bio-natural gas. The fossil share does not include fossil fuels used for electricity and district heating production.

## Slide 13: Figure 15: Industry and services energy consumption for heat pumps [PJ].

## Slide 14: Figure 16: Energy intensity in industry and services by industry 2017-2030 [PJ/DKK bn.].

## Slide 15: Figure 17: Final energy consumption by the transport sector by use 2017-2030 [PJ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Road | 162.2145 | 163.6366 | 165.0438 | 166.0638 | 166.7186 | 167.1441 | 167.4333 | 167.5713 | 167.5021 | 167.2164 | 166.7333 | 166.0493 | 165.1512 | 164.0344
Aviation | 42.2626 | 42.4645 | 42.7098 | 42.865 | 43.0797 | 43.3334 | 43.5689 | 43.8105 | 44.0183 | 44.2772 | 44.6023 | 44.8854 | 45.1741 | 45.5517
Rail | 4.7621 | 4.8163 | 4.8623 | 4.9083 | 4.9331 | 4.9391 | 4.9661 | 4.9135 | 4.919 | 4.9247 | 4.652 | 4.6828 | 4.7346 | 4.7679
Military | 2.7997 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538 | 2.8538
Maritime | 6.2141 | 6.1921 | 6.1702 | 6.1483 | 6.1264 | 6.1045 | 6.0826 | 6.0607 | 6.0388 | 6.0168 | 5.9949 | 5.973 | 5.9511 | 5.9292

## Slide 16: Figure 18: Electricity consumption by the transport sector by area of use 2017-2030 [PJ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Light road | 0 | 0.19 | 0.26 | 0.38 | 0.52 | 0.66 | 0.81 | 0.96 | 1.16 | 1.41 | 1.74 | 2.16 | 2.67 | 3.29
Heavy road | 0 | 0 | 0.01 | 0.03 | 0.05 | 0.07 | 0.09 | 0.12 | 0.15 | 0.18 | 0.22 | 0.26 | 0.3 | 0.34
Rail | 1.47 | 1.51 | 1.55 | 1.59 | 1.61 | 1.61 | 1.63 | 1.96 | 1.96 | 1.96 | 3.53 | 3.66 | 3.79 | 3.82
Maritime | 0 | 0 | 0.01 | 0.01 | 0.02 | 0.02 | 0.03 | 0.03 | 0.04 | 0.04 | 0.05 | 0.05 | 0.06 | 0.06

## Slide 17: Figure 19: Electrified vehicles' share of sales of new vehicles and share of total number of passenger cars and vans on the road 2017-2030 [%].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Electric vehicles (EV, BEV) | 0.0030394 | 0.0087662 | 0.016837 | 0.023551 | 0.026726 | 0.029078 | 0.031954 | 0.038615 | 0.050353 | 0.065266 | 0.082668 | 0.10202 | 0.1233 | 0.14539
Plug-in hybrids (PHEV) | 0.0024097 | 0.013843 | 0.018262 | 0.021723 | 0.02438 | 0.024877 | 0.023895 | 0.025363 | 0.029711 | 0.035198 | 0.041966 | 0.050059 | 0.059538 | 0.069794
Share of total vehicle stock | 0.0038283 | 0.0058263 | 0.0081267 | 0.011183 | 0.014609 | 0.018158 | 0.021751 | 0.025897 | 0.03123 | 0.038084 | 0.046723 | 0.057384 | 0.070283 | 0.085497

## Slide 18: Figure 20: Renewable energy consumption by the transport sector 2017-2030 [PJ ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Bio-natural gas | 0.013927 | 0.017729 | 0.024532 | 0.044071 | 0.055284 | 0.070735 | 0.079224 | 0.090261 | 0.10178 | 0.11491 | 0.12815 | 0.14062 | 0.15108 | 0.16019
First gen. bio-fuels | 8.8998 | 8.9784 | 9.1447 | 7.6716 | 7.7949 | 7.9109 | 8.0249 | 8.1341 | 8.2265 | 8.2983 | 8.3516 | 8.3749 | 8.3636 | 8.3285
Second gen. bio-fuels | 0.12 | 0.12 | 0.12 | 1.4751 | 1.4853 | 1.4955 | 1.5044 | 1.5074 | 1.5082 | 1.5078 | 1.5024 | 1.4983 | 1.4919 | 1.4666
Electricity (RE share) | 0.93421 | 1.2077 | 1.3362 | 1.5437 | 1.765 | 2.0055 | 2.1905 | 2.7013 | 2.9277 | 3.5376 | 5.501 | 6.1319 | 6.8206 | 7.5135

## Slide 19: Figure 21: Location of coal-fired electricity production plants and offshore wind turbines.

## Slide 20: Figure 22: Consumption of energy by the electricity and district heating sector, by type of energy 2017-2030 [PJ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Ambient heat | 0.15247 | 0.69769 | 0.97467 | 1.2711 | 3.4622 | 5.2757 | 6.391 | 7.2731 | 8.1238 | 8.2185 | 8.6341 | 9.3133 | 9.883 | 10.0063
Solar | 4.4379 | 5.2676 | 5.7095 | 6.5525 | 8.5273 | 10.7984 | 13.0766 | 15.3621 | 18.1456 | 20.1229 | 21.8856 | 23.537 | 25.2146 | 26.958
Bioenergy | 131.9127 | 148.8412 | 149.4501 | 153.2716 | 152.959 | 151.6257 | 151.1027 | 149.9738 | 147.9059 | 146.2038 | 145.2527 | 144.1476 | 143.3001 | 142.0008
Wind power | 53.208 | 57.9942 | 62.2701 | 66.5862 | 73.5435 | 82.7572 | 86.5113 | 91.891 | 94.7384 | 111.1545 | 115.9608 | 122.1311 | 127.6734 | 138.2887
Fossil fuels | 127.2443 | 84.137 | 83.2113 | 67.4043 | 55.9703 | 51.1576 | 37.3934 | 37.085 | 36.3839 | 35.5631 | 33.6522 | 32.2028 | 17.9691 | 17.5615

## Slide 21: Figure 23: Renewables share in electricity consumption (RES-E) by wind power, solar PV, bioenergy and hydropower 2017-2030 [%]. Hydropower is very small and has been included in solar PV.
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Bioenergy | 0.17516 | 0.21724 | 0.21074 | 0.21979 | 0.2139 | 0.20063 | 0.1903 | 0.18285 | 0.17631 | 0.17042 | 0.16349 | 0.15825 | 0.15241 | 0.14724
Solar power | 0.026986 | 0.029023 | 0.029413 | 0.034901 | 0.046018 | 0.058269 | 0.069951 | 0.08108 | 0.092 | 0.10233 | 0.10986 | 0.11737 | 0.12469 | 0.13211
Wind power | 0.432 | 0.46044 | 0.4859 | 0.51125 | 0.54423 | 0.58893 | 0.59536 | 0.61329 | 0.61642 | 0.70906 | 0.71857 | 0.74256 | 0.76145 | 0.80932
100 pct. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 22: Figure 24: Electricity consumption, including transmission and distribution losses, electricity production and electricity imports 2017-2030 (TWh).
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Electricity production | 29.6761 | 32.619 | 33.8707 | 34.5612 | 36.126 | 38.7137 | 38.8564 | 40.8802 | 42.0627 | 46.9141 | 48.3972 | 50.3 | 50.4025 | 53.6407
Electricity imports | 4.5627 | 2.3685 | 1.7273 | 1.6168 | 1.4109 | 0.32005 | 1.5074 | 0.74005 | 0.62914 | -3.3685 | -3.5705 | -4.6132 | -3.8273 | -6.1769
Electricity consumption incl. grid losses | 34.2388 | 34.9875 | 35.598 | 36.178 | 37.5369 | 39.0338 | 40.3638 | 41.6202 | 42.6919 | 43.5455 | 44.8267 | 45.6869 | 46.5752 | 47.4638

## Slide 23: Figure 25: Electricity spot market prices for Denmark and selected price-setting markets 2017-2030 [2019 DKK/MWh]. Prices for all the years are model results. The Danish Energy Agency uses statistical prices and forward prices for 2017-2020. NO: Norway, SE: Sweden, FI: Finland, DE-AT-LU: Germany, Austria, Luxembourg, NL: The Netherlands, GB: Great Britain, FR-BE: Belgium, DK: Denmark.
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
NO | 235.5107 | 278.6069 | 252.4785 | 251.3936 | 281.0917 | 280.3444 | 290.5975 | 296.0952 | 301.5131 | 298.8609 | 300.8955 | 293.4881 | 293.4328 | 292.6132
SE | 234.4366 | 284.9798 | 271.9082 | 263.4986 | 286.9514 | 286.0122 | 295.6997 | 299.261 | 303.8311 | 301.0143 | 304.4265 | 297.0268 | 297.8995 | 297.4522
FI | 243.9224 | 292.4689 | 282.895 | 260.8452 | 281.6391 | 281.2686 | 293.6509 | 297.2067 | 302.2262 | 302.2488 | 307.2444 | 297.8922 | 300.937 | 305.7799
DE-AT-LU | 279.6862 | 389.1381 | 389.2012 | 364.8471 | 350.1978 | 352.7787 | 361.0743 | 364.5305 | 370.867 | 369.1886 | 366.6526 | 367.0751 | 369.8037 | 368.9587
NL | 286.5355 | 411.3789 | 394.8373 | 360.2973 | 343.4506 | 344.61 | 352.3608 | 356.896 | 365.405 | 364.0312 | 361.8875 | 363.5349 | 366.9492 | 366.8227
GB | 377.5457 | 466.7776 | 454.8713 | 399.1589 | 358.9679 | 353.3936 | 354.8126 | 356.7276 | 361.8343 | 357.6638 | 353.4238 | 369.1205 | 370.2699 | 368.7729
FR-BE | 310.9878 | 424.7871 | 399.1333 | 364.7486 | 343.5623 | 346.4489 | 355.1096 | 357.6562 | 369.177 | 368.4345 | 368.6185 | 373.0343 | 383.8207 | 390.8893
DK | 242.2071 | 318.3563 | 320.3674 | 326.8758 | 326.7043 | 326.3992 | 337.9674 | 350.3468 | 358.4513 | 352.4967 | 350.5153 | 347.5882 | 349.0077 | 344.2326

## Slide 24: Figure 26: Availability of coal plants in the projection 2017-2030. Light grey shows that operation of the relevant plant is expected to be limited in the relevant period.

## Slide 25: Figure 27: Small-scale electricity production capacity (>0) and electricity consumption capacity for heat production (<0) in small and medium-sized urban areas 2017-2030 [MW electricity].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Oil | 127.5204 | 127.5204 | 127.4917 | 127.4917 | 120.5868 | 113.6819 | 106.7771 | 106.7771 | 106.7771 | 106.7771 | 106.7771 | 106.7771 | 106.7771 | 106.7771
Bioenergy | 68.4611 | 68.9062 | 72.9604 | 72.9604 | 71.2585 | 68.6066 | 65.9546 | 62.2721 | 62.2721 | 62.2721 | 62.2721 | 62.2721 | 62.2721 | 62.2721
Gas | 1190.5322 | 1136.9571 | 1181.245 | 1181.245 | 1115.076 | 990.6556 | 952.2113 | 910.8297 | 793.4456 | 762.379 | 755.5731 | 715.644 | 671.8461 | 606.6942
Electric boilers | -303.24 | -303.24 | -330.24 | -348.24 | -348.24 | -348.24 | -348.24 | -348.24 | -348.24 | -348.24 | -348.24 | -348.24 | -348.24 | -348.24
Coal | 3.8831 | 3.8831 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Heat pumps | -6.5837 | -6.8623 | -9.6072 | -19.9509 | -49.4946 | -75.0124 | -100.8981 | -126.4159 | -151.9337 | -152.9781 | -154.0226 | -155.067 | -156.1115 | -157.1559

## Slide 26: Figure 28: Consumption of fossil fuels in the electricity and district heating sector 2017-2030 [PJ].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
MSW (fossil share) | 16.8566 | 17.7183 | 17.4855 | 17.4639 | 17.4706 | 17.4472 | 17.4436 | 17.4437 | 16.9282 | 16.9127 | 16.8996 | 16.8894 | 16.8675 | 16.475
Oil | 4.3602 | 3.8497 | 4.0215 | 3.2417 | 3.0381 | 3.0528 | 2.9715 | 3.0014 | 2.9966 | 2.9522 | 2.9344 | 2.9497 | 2.6128 | 2.6045
Natural gas | 37.7539 | 23.4141 | 19.0173 | 18.8837 | 18.1832 | 14.2351 | 12.4496 | 10.6704 | 9.716 | 9.1236 | 8.6779 | 8.3435 | 8.2807 | 7.9942
Coal | 85.1303 | 56.8732 | 60.1724 | 45.2789 | 34.749 | 33.8697 | 21.9723 | 23.4132 | 23.6713 | 23.4873 | 22.0399 | 20.9096 | 7.0756 | 6.9629

## Slide 27: Figure 29: Domestic electricity production by type of production, and share of electricity imports in total electricity production [%].
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Co-generation | 49.7983 | 46.1767 | 43.3248 | 41.8163 | 42.6442 | 40.0319 | 37.9555 | 37.249 | 36.4636 | 36.2186 | 35.2497 | 34.2118 | 32.4441 | 31.8062
Condensing | 5.9349 | 9.5395 | 12.4933 | 11.4895 | 7.6419 | 8.3442 | 5.1663 | 5.7747 | 5.9616 | 5.3451 | 5.1507 | 5.2832 | 0.26579 | 0.26917
Wind power | 53.2479 | 57.9942 | 62.2701 | 66.5862 | 73.5435 | 82.7572 | 86.5113 | 91.891 | 94.7384 | 111.1545 | 115.9608 | 122.1311 | 127.6734 | 138.2887
Solar power | 3.262 | 3.5914 | 3.705 | 4.4812 | 6.1543 | 8.1237 | 10.1003 | 12.0842 | 14.0753 | 15.9771 | 17.6642 | 19.24 | 20.8422 | 22.51
Import | 0.15375 | 0.072611 | 0.050998 | 0.046782 | 0.039054 | 0.008267 | 0.038794 | 0.018103 | 0.014957 | -0.071802 | -0.073775 | -0.091713 | -0.075934 | -0.11515

## Slide 28: Figure 30: District heating production by type of energy and renewables share in district heating 2017-2030 [PJ]. Heat pumps cover production from ambient heat and surplus heat. Surplus heat is without use of heat pumps.
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
MSW | 27.072 | 27.2793 | 27.1707 | 27.1418 | 27.1584 | 27.1186 | 27.1119 | 27.1123 | 26.3622 | 26.3398 | 26.3218 | 26.3082 | 26.2737 | 25.6342
Biogas | 2.2836 | 2.2736 | 2.2695 | 2.2638 | 2.2637 | 2.2636 | 2.2633 | 2.2632 | 2.2629 | 2.261 | 2.2589 | 2.2574 | 2.2553 | 2.2533
Solar heat | 1.5797 | 1.6762 | 2.0045 | 2.0713 | 2.373 | 2.6746 | 2.9763 | 3.2779 | 4.0703 | 4.1458 | 4.2214 | 4.2969 | 4.3725 | 4.448
Industrial waste heat | 5.0006 | 5.0199 | 5.1463 | 5.4949 | 5.7192 | 6.5416 | 6.633 | 7.0556 | 7.1656 | 7.18 | 7.1907 | 7.1977 | 7.3783 | 7.4111
Biomass | 54.1712 | 63.3853 | 66.3316 | 70.5621 | 70.0733 | 69.6651 | 70.5056 | 70.0817 | 69.5968 | 68.4879 | 68.0364 | 67.5018 | 67.4256 | 67.4631
Coal | 21.9431 | 13.8888 | 11.6507 | 8.132 | 7.6609 | 6.6746 | 5.2649 | 5.3257 | 5.2733 | 5.8427 | 5.3953 | 4.7883 | 3.484 | 3.4282
Natural gas (and oil) | 21.4263 | 17.7108 | 15.4019 | 14.8043 | 12.6263 | 10.3855 | 8.8169 | 7.2108 | 6.4227 | 6.2836 | 6.16 | 6.0081 | 6.0606 | 5.9544
Heat pumps (and el. boilers) | 1.5665 | 3.0571 | 3.5669 | 2.3303 | 4.8849 | 7.401 | 9.118 | 10.3258 | 11.4632 | 11.6881 | 12.2586 | 13.0968 | 13.8178 | 14.0888
RE Share (RES-DH) [%] | 0.55051 | 0.63848 | 0.67184 | 0.70725 | 0.72392 | 0.74394 | 0.76282 | 0.76898 | 0.77571 | 0.7741 | 0.77782 | 0.78276 | 0.79034 | 0.79282

## Slide 29: Figure 31: Consumption of mains gas broken down by natural gas and bio-natural gas 2017-2030 [PJ], and the share of bio-natural gas in mains gas [%]. The calculation is based on bio-natural gas produced in relation to the domestic consumption of mains gas.
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Bio-natural gas | 5.0176 | 5.676 | 7.9312 | 12.5605 | 13.5512 | 18.5019 | 18.5029 | 18.5037 | 18.5046 | 18.509 | 18.5138 | 18.5178 | 18.5225 | 18.5272
Natural gas | 95.7892 | 86.6295 | 80.0934 | 76.3175 | 74.6993 | 66.3622 | 64.1024 | 61.8315 | 60.5666 | 59.5241 | 58.661 | 57.9322 | 57.5382 | 56.8527
Share of bio-natural gas in piped gas [%] | 0.049775 | 0.061491 | 0.090102 | 0.14132 | 0.15355 | 0.21802 | 0.22399 | 0.23033 | 0.23402 | 0.23719 | 0.23989 | 0.24222 | 0.24352 | 0.24578

## Slide 30: Figure 32: Emissions of greenhouse gases by sector from 1990-2030 and in the 1990 UN base year [mill. tonnes CO2-eq.]. The statistical calculation of the area chart for 1990-2017 has been adjusted for electricity trade with other countries (electricity-trade adjusted (Appendix 2)). Reduction targets are based on observed (actual) emissions relative to the UN base year and excluding LULUCF. LULUCF emissions are calculated separately and are not included here.
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Transport | 11.8292 | 12.5623 | 12.6034 | 12.7433 | 13.162 | 13.281 | 13.4694 | 13.6119 | 13.6295 | 13.5872 | 13.3596 | 13.381 | 13.5059 | 13.9595 | 14.3103 | 14.5242 | 14.6671 | 15.2246 | 14.9684 | 14.2113 | 14.0108 | 13.7372 | 13.0529 | 12.8604 | 12.9434 | 13.1738 | 13.4636 | 13.7558 | 13.653 | 13.725 | 13.7881 | 13.8045 | 13.8049 | 13.7953 | 13.7433 | 13.7029 | 13.642 | 13.4249 | 13.3272 | 13.2111 | 13.0809
Agriculture | 12.6681 | 12.5064 | 12.3403 | 12.2905 | 12.1275 | 12.1292 | 11.7028 | 11.7163 | 11.707 | 11.3589 | 11.2563 | 11.2494 | 11.3269 | 11.0695 | 11.0073 | 10.8135 | 10.554 | 10.7835 | 10.7297 | 10.4868 | 10.4046 | 10.3947 | 10.3705 | 10.3505 | 10.5237 | 10.3968 | 10.5742 | 10.6417 | 10.7458 | 10.5797 | 10.4275 | 10.4151 | 10.4249 | 10.4193 | 10.418 | 10.4106 | 10.4168 | 10.4252 | 10.4275 | 10.4403 | 10.4773
Other | 4.1057 | 4.2413 | 4.2764 | 4.3533 | 4.4049 | 4.4982 | 4.5959 | 4.606 | 4.689 | 5.0256 | 5.1855 | 5.058 | 5.0253 | 5.0336 | 4.5516 | 4.0107 | 4.1262 | 4.1492 | 3.8194 | 3.3517 | 3.0699 | 3.205 | 3.1947 | 3.1315 | 3.0855 | 2.8983 | 3.134 | 3.1395 | 3.2562 | 3.1808 | 2.9748 | 2.9322 | 2.9523 | 2.9623 | 2.9742 | 2.9794 | 2.9773 | 2.9705 | 2.9581 | 2.9403 | 2.9243
Households | 5.1441 | 5.4025 | 4.816 | 5.5597 | 5.0987 | 5.1457 | 5.5103 | 4.9469 | 4.8533 | 4.6642 | 4.1777 | 4.3845 | 4.1255 | 4.1028 | 3.9634 | 3.8537 | 3.6148 | 3.3755 | 3.257 | 3.1649 | 3.3823 | 2.8672 | 2.673 | 2.5806 | 2.0659 | 2.1698 | 2.1999 | 2.0534 | 2.1785 | 2.0547 | 1.899 | 1.8195 | 1.6673 | 1.5999 | 1.5323 | 1.4685 | 1.4059 | 1.3441 | 1.283 | 1.2234 | 1.1628
Industry and services | 11.752 | 12.6945 | 12.5364 | 12.3811 | 12.4387 | 12.7665 | 13.3538 | 13.3458 | 12.9204 | 13.8993 | 13.2257 | 13.3441 | 12.8509 | 12.9288 | 13.0225 | 12.4172 | 12.5624 | 12.0493 | 11.2069 | 9.9739 | 10.4833 | 9.8646 | 9.4578 | 9.2577 | 8.8678 | 9.0363 | 8.933 | 9.0297 | 8.6496 | 8.4335 | 7.9611 | 7.9248 | 8.0238 | 8.1919 | 8.245 | 8.1452 | 7.7495 | 7.7523 | 7.7633 | 7.7415 | 7.784
Electricity and district heating | 31.0165 | 32.0559 | 31.3535 | 31.0914 | 30.2411 | 29.7555 | 29.67 | 27.6347 | 26.2817 | 24.8267 | 24.2376 | 24.5471 | 23.4708 | 22.9491 | 21.6098 | 21.7424 | 22.8222 | 22.9765 | 22.8917 | 21.9949 | 20.7756 | 18.8118 | 18.6798 | 17.4133 | 15.0167 | 14.0515 | 14.9098 | 11.9688 | 8.5595 | 8.6085 | 7.1466 | 6.1021 | 5.7958 | 4.5578 | 4.5825 | 4.5005 | 4.4433 | 4.2778 | 4.1476 | 2.8061 | 2.7417
UN Base Year 1990 | 70.8019
Actual emissions | 70.2897 | 81.0023 | 75.0169 | 77.3634 | 81.258 | 78.2572 | 91.3316 | 81.7984 | 77.7561 | 75.2589 | 70.7883 | 72.3308 | 71.8956 | 76.849 | 70.6819 | 66.229 | 73.9513 | 69.3253 | 65.7031 | 62.9162 | 63.0368 | 57.8112 | 53.2199 | 54.9216 | 50.7453 | 48.1319 | 50.1527 | 47.8889

## Slide 31: Figure 33: Non-ETS emissions 2005-2020 and reduction commitment 2013-2020 [mill. tonnes CO2-eq.]
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Non-ETS emissions | 39.7533 | 39.7182 | 39.8851 | 39.157 | 36.9018 | 37.7704 | 36.3456 | 35.0344 | 33.1785 | 32.2194 | 32.2058 | 32.7982 | 32.6734 | 33.1198 | 32.5939 | 31.9752
Reduction path 2013-2020 | 36.8292 | 35.9252 | 35.0212 | 34.1172 | 34.7756 | 33.8714 | 32.9672 | 32.063

## Slide 32: Figure 34: Non-ETS emissions 2005-2030, reduction commitment and accumulated shortfall 2021-2030 [mill. tonnes CO2-eq.].
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Accumulated shortfall | 0.15711 | 0.82599 | 2.1568 | 4.1161 | 6.7053 | 9.9043 | 13.5894 | 17.8741 | 22.7509 | 28.234
Non-ETS emissions | 39.7533 | 39.7182 | 39.8851 | 39.157 | 36.9018 | 37.7704 | 36.3456 | 35.0344 | 33.1785 | 32.2194 | 32.2058 | 32.7982 | 32.6734 | 33.1198 | 32.5939 | 31.9752 | 31.7321 | 31.43 | 31.2779 | 31.0925 | 30.9085 | 30.7043 | 30.3764 | 30.1621 | 29.9403 | 29.7326
Reduction path 2021-2030 | 31.575 | 30.7611 | 29.9471 | 29.1332 | 28.3192 | 27.5053 | 26.6913 | 25.8774 | 25.0635 | 24.2495

## Slide 33: Figure 35: LULUCF emissions and sinks 1990-2030 [mill. tonnes CO2-eq.]
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
LULUCF net emissions | 4.9404 | 4.34 | 5.4505 | 4.4297 | 3.759 | 3.7342 | 3.1671 | 3.4808 | 3.3341 | 3.4854 | 3.5743 | 4.0739 | 5.0223 | 4.7349 | 4.4467 | 4.3519 | 4.7143 | 2.2147 | -2.2804 | 1.996 | -0.94579 | -2.5245 | -0.66865 | 0.48013 | 0.21147 | 3.8037 | 4.6762 | 3.133 | 4.283 | 4.2639 | 2.5265 | 2.0229 | 2.5524 | 2.6044 | 2.8888 | 2.3053 | 3.2207 | 3.0563 | 2.9682 | 2.7573 | 3.3445

## Slide 34: Figure 36: CO2 emissions from industry and services in 2030 by energy service and type of fuel [mill. tonnes CO2].

## Slide 35: Figure 37: Difference between central scenario and partial sensitivities in the total share of renewables (RES). Red bars show reduced renewables shares; green bars show increased renewables shares.
Chart: 
| A. Data centers | B. Carbon ETS price | C. RE-deployment | D. Electrified vehicles | E. Energy eff. industry/services | F. Dairy cattle | G. Aviation biofuels | H. Coal-fired electricity
Høj | 1.5946 | 0.54067 | 0.88659 | 0.38955 | 0 | 0 | 0.64075 | 0.15119
Lav | 0 | -0.16418 | -3.6303 | -0.19237 | -0.016643 | 0 | 0 | -0.04853

## Slide 36: Figure 38: Difference between central scenario and partial sensitivities in emissions broken down by ETS and non-ETS [mill. tonnes CO2-eq.]. Green bars show reduced emissions; red bars show increased emissions.
Chart: 
| A. Data centers | B. Carbon ETS price | C. RE-deployment | D. Electrified vehicles | E. Energy eff. industry/services | F. Dairy cattle | G. Aviation biofuels | H. Coal-fired electricity
ETS | -0.024454 | -0.22737 | -0.0062402 | -0.0013068 | -0.041852 | 0 | -0.015578 | -0.58403
Non-ETS | -0.0047992 | -0.036759 | -0.0010392 | -0.64254 | -0.064501 | -0.5 | 0 | -0.037633
ETS | 0 | 0.083886 | 0.020677 | 0.0023402 | 0.019587 | 0 | 0 | 2.1804
Non-ETS | 0 | 0.14881 | 0.0030073 | 0.32127 | 0.021976 | 0.5 | 0 | 0.043386